| U Value Table |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Element/Material | Conductivity (K) | Resistivity (1/K) | Thickness (m) | Resistance ( R ) |  |
| Ext. Surface R |  |  |  | 0.053 |  |
| Int. Surface R |  |  |  | 0.123 |  |
| Cavity R |  |  |  | 0.176 |  |
| Facing Brick | 1.47 | 0.680272109 | 0.1 | 0.068027211 |  |
| Common Brick | 1.21 | 0.826446281 | 0.1 | 0.082644628 |  |
| Plaster Int. | 0.5 | 2 | 0.02 | 0.04 |  |
|  |  |  | Total R | 0.542671839 |  |
|  |  | U Value | 1/Total R = | 1.842734279 | W/m² ºC |

To calculate the Rate of Heat Loss,  Formula

U Value  X  Area  X  Temperature Difference  = Heat Loss( Watts or Joules / second)

1.8427  x  1  X  20  =  36.854 Watts / Joules/sec.