U Value 2001

U Value of Single Glazing

| Element/Material | Conductivity (K) | Resistivity (1/K) | Thickness (m) | Resistance ( R ) |  |
| --- | --- | --- | --- | --- | --- |
| Ext. Surface R |  |  |  | 0.08 |  |
| Int. Surface R |  |  |  | 0.12 |  |
| 4mm Glass | 1.02 | 0.980 | 0.004 | 0.00392 |  |
|  |  |  | Total R | 0.20392 |  |
|  |  | U Value | 1/Total R = | 4.90388 | w/msK |

U Value of Double Glazing

| Element/Material | Conductivity (K) | Resistivity (1/K) | Thickness (m) | Resistance ( R ) |  |
| --- | --- | --- | --- | --- | --- |
| Ext. Surface R |  |  |  | 0.08 |  |
| Int. Surface R |  |  |  | 0.12 |  |
| Air Space |  |  |  | 0.17 |  |
| 4mm Glass | 1.02 | 0.980 | 0.004 | 0.00392 |  |
| 4mm Glass | 1.02 | 0.980 | 0.004 | 0.00392 |  |
|  |  |  | Total R | 0.37784 |  |
|  |  | U Value | 1/Total R = | 2.64662 | w/msK |

Rate of Heat Loss through Single glazing,  =  4.903  X  20  X  8  =  784.6208 W/sec

Daily Energy Loss ( W X Secs)  = 784.6208  X  24 X 60 X 60 = 67791.2371 KJ

Rate of Heat Loss through Double glazing, =  2.64662  X  20  X  8 =  423.4592 W/sec

Daily Energy Loss  ( W X Secs)  =  423.4592  X 24  X  60  X  60  =  36586.8749 KJ

Difference in Daily Energy Loss  =  67791.2371 - 36586.8749  = 31204.3622 KJ

Reduction in Oil requirement        =   31204.3622      =  0.8355 Litres

37350

Daily Savings                                 =  0.8355  X  40  =  33.42 p

Homework.

Calculate the daily savings for a glazing panel (Window) which meets current regulations ( U value of 1.6 w/m²) compared with single glazing. Use the same calorific value for oil and at a cost of 87cent / litre.