U Value 2008

Part A

| U Value Table |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Single Glazing |  |  |  |  |  |
| Element/Material | Conductivity (K) | Resistivity (1/K) | Thickness (m) | Resistance ( R ) |  |
| Int. Surface R |  |  |  | 0.122 |  |
| Ext. Surface R |  |  |  | 0.080 |  |
| Glass | 1.020 | 0.9803 | 0.005 | 0.0049 |  |
|  |  |  | Total R | 0.2069 |  |
|  |  | U Value | 1/Total R = | 4.833 |  |

| U Value Table |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Double Glazing |  |  |  |  |  |
| Element/Material | Conductivity (K) | Resistivity (1/K) | Thickness (m) | Resistance ( R ) |  |
| Int. Surface R |  |  |  | 0.122 |  |
| Ext. Surface R |  |  |  | 0.080 |  |
| Cavity |  |  |  | 0.170 |  |
| Glass | 1.020 | 0.9803 | 0.006 | 0.00588 |  |
| Glass | 1.020 | 0.9803 | 0.006 | 0.00588 |  |
|  |  |  | Total R | 0.38376 |  |
|  |  | U Value | 1/Total R = | 2.60579 |  |

Part B

Calculate the rate of heat loss

Area ( m² ) x  Temp. diff  x  u value  =   w/sec  or  Joules / sec

X      X     =   w/sec  or  Joules / sec

Use the Heating period    and    multiply by rate of heat loss

Heating period per annum

12  X  7  X  40 = 3,360

6o  x  6o  x  3,360   =  12,096,000  X 665.28 divided by 1000 to get Kw/KJ

=  8,047,226.88 Kj

1 litre of Oil   =  37,350 KJ

Therefore

8,047,226.88  divided by 37,350  =  no. of litre  =  215.45 Litres

@ 0.85 cent / Litre =  € 183.14c  = annual heating cost

Part C