U Value 2010

Part A

| U Value Table |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Element/Material | Conductivity (K) | Resistivity (1/K) | Thickness (m) | Resistance ( R ) |  |
| Ext. Surface R |  |  |  | 0.048 |  |
| Int. Surface R |  |  |  | 0.122 |  |
| Solid wall |  | 1.190 | 0.225 | 0.267 |  |
| Plaster Int |  | 6.250 | 0.013 | 0.081 |  |
| Ext. Render |  | 2.170 | 0.016 | 0.035 |  |
|  |  |  | Total R | 0.553 |  |
|  |  | U Value | 1/Total R = | 1.8083 | W/m² ºC |

Part B

Calculate the thickness of phenolic foam required to achieve a u value of 0.27 W/m² ºC

K value of foam = 0.025

Existing u value = 1.8083,   R = 0.553

Required u value = 0.27,      R = 3.7037

3.7037 – 0.553 =  3.1507= Required R using foam

40 X thickness (x) = 3.1507

X = 3.1507  divided  40 =  0.07876 = 0.079 m =  79mm

Part C