U Value 2011

Part A

| U Value Table |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Element/Material | Conductivity (K) | Resistivity (1/K) | Thickness (m) | Resistance ( R ) |  |
| Ext. Surface R |  |  |  | 0.048 |  |
| Int. Surface R |  |  |  | 0.104 |  |
| Hollow Block R |  |  |  | 0.210 |  |
| Airspace R |  |  |  | 0.170 |  |
| Ext. Render |  | 2.170 | 0.015 | 0.03255 |  |
| Int. Plasterboard | 0.160 | 6.25 | 0.012 | 0.075 |  |
|  |  |  | Total R | 0.63955 |  |
|  |  | U Value | 1/Total R = | 1.5635 |  |

Part B

Calculate the thickness of expanded polystyrene required

to achieve a u value of 0.27

K value of expanded polystyrene = 0.037, 1/k = 27.027

Existing u value = 1.5635,   R =  0.63955

Required u value = 0.27,      R = 3.7037

3.7037 – 0.63955  =  3.06415  Required R using foam

27.027  X thickness (T) = 3.06415

T = 3.06415  divided  27.027 =  0.113 m =  113 mm

Part C